## Slide 1
Test Automation
ZL Chen, SIoT DQA, Advantech

## Slide 2: Agenda
What is Test Automation?
What is the Test Automation Pyramid?
What is difference between Test Automation and Automation Testing?
Automation Testing Tools for Introduction & Demo

## Slide 3: What is Test Automation?
In software testing, test automation is the use of software separate from the software being tested to control the execution of tests and the comparison of actual outcomes with predicted outcomes.
Test automation can automate some repetitive but necessary tasks in a formalized testing process already in place, or perform additional testing that would be difficult to do manually. Test automation is critical for continuous delivery and continuous testing.

## Slide 4
Why Automation Needs Humans?
Why Automation?
Why Automation is NOT easy?
Why Automation Testing is important?
Why ???

## Slide 5: Why Automated Testing?
Automated testing is important due to following reasons:
  Manual Testing of all work flows, all fields, all negative scenarios is time and cost consuming.
  It is difficult to test for multilingual sites manually.
  Automation does not require human intervention.
    You can run automated test unattended (overnight).
  Automation increases speed of test execution & test coverage.
  Manual testing can become boring and hence error prone.

## Slide 6: What is Test Automation Pyramid?
There are many approaches to test automation, however below are the general approaches used widely:
  Graphical user interface testing
  API driven testing
  Unit testing

## Slide 7: What is difference between Test Automation and Automation Testing?
Automated testing is the act of conducting specific tests via automation as opposed to conducting them manually. Just like a set of regression tests.
Test automation refers to automating the process of tracking and managing the different tests.

## Slide 8: Automation Testing Tools for Introduction & Demo
Roaming automation
Wi-Fi frequency switch automation (2.4G, 5G)
Airplane on/off mode automation
  Android 6.0.1 (RJ-45), Android 6.0.1 (OTG) for WLAN and WWAN
  Android 8.1.0 (RJ-45), Android 8.1.0 (OTG) for WLAN and WWAN
  Windows for WLAN
Resolution automation
Luminance automation
PXE automatic installation
BurnInTest automation
ProgramIndex automation
Continuous Integration

## Slide 9: Roaming automation
System Structure

## Slide 10: Roaming automation – Selenium Web driver
Selenium’s web driver application and infrastructure

## Slide 11: Roaming automation
The roaming’s log as below:

## Slide 12: Roaming automation
The roaming’s ping log as below:

## Slide 13: Roaming automation
結論
  減少手動測試失誤問題
  省去手動切換 AP 行為
  準確擷取 Ping 紀錄檔
  長時間壓力測試執行

## Slide 14: Wi-Fi frequency switch automation (2.4G, 5G)
  System Structure

## Slide 15: Wi-Fi frequency switch automation (2.4G, 5G)
The Wi-Fi switch’s screenshot and log as below:

## Slide 16: Wi-Fi frequency switch automation (2.4G, 5G)
結論
  針對 Wi-Fi Mode 中的 2.4 G 中的 N Only, Legacy 相互切換
  針對 Wi-Fi Mode 中的 5 G 中的 N/AC mixed, Legacy 相互切換
  長時間做 2.4 G 及 5 G 之壓力測試

## Slide 17: Airplane on/off mode automation
  Android 6.0.1 (RJ-45), Android 6.0.1 (OTG) for WLAN and WWAN
  System Structure

## Slide 18: Airplane on/off mode automation
  Android 8.1.0 (RJ-45), Android 8.1.0 (OTG) for WLAN and WWAN
  System Structure

## Slide 19: Airplane on/off mode automation
  Windows for WLAN
  System Structure

## Slide 20: Airplane on/off mode automation
  Conclusion

## Slide 21: Resolution automation
  The Tool base on the GPU resolution
  Auto catch the resolution by batch code
  Auto catch the resolution by batch code. (Reboot)
  結論
    透過程式自動擷取主機 GPU 解析度
    長時間重開機解析度擷取

## Slide 22: Luminance automation
  The tool of pre-conditions base on the product specification.
    Width
    Height
    Aliquots
    Pixel Pitch
    Point
    Edge

## Slide 23: Luminance automation
  The output luminance photo.

## Slide 24: Luminance automation
  結論
    依產品需求規格製作產圖之程式
    方便內部人員快速產圖並做量測 Panel 、明暗度之程式

## Slide 25: PXE automatic installation
  System Structure

## Slide 26: PXE automatic installation
  Operation System
    Windows Server 2012 R2 for Legacy 32 bits
    Windows Server 2012 R2 for Legacy 64 bits
    Windows Server 2012 R2 for UEFI 64 bits
  結論
    自動化安裝 Windows OS 程序
    長時間自動安裝壓力測試

## Slide 27: PXE automatic installation
  結論
    自動化安裝 Windows OS 程序
    長時間自動安裝壓力測試

## Slide 28: BurnInTest automation
  The tool of pre-conditions base on the exe script.
    bit.exe -c dqa.bitcfg -r -p -D “minutes”

## Slide 29: BurnInTest automation
  結論
    透過 BurnInTest 的 Bash Script 做長時間壓力測試
    自動產生及備份 Log 檔案

## Slide 30: ProgramIndex automation
  Download the file by ProgramIndex user interface.
    Server IP
    Suite Folder
    Case Folder
    Downlod

## Slide 31: ProgramIndex automation
  結論
    透過 ProgramIndex 程式方便下載相對應程式
    可以直接抓取 FTP 上的資料直接下載

## Slide 32: Continuous Integration
  System Structure

## Slide 33: Continuous Integration
  CI is as natural as the Enter key on the keyboard. In every change, the CI server helps us integrate all relevant services and feeds the results back to the entire team, just like a doctor is helping the system to be healthy all the time to examination.
  Conclusion
  Auto build source code
  Automated Testing
  Code analysis
  Automatic deployment
  Database integration

## Slide 34: Automation Tools hyperlink
\\172.17.9.225\dqa\iService\0G.DQA_Zone\50.Auto Test Tool\automation\suite

## Slide 35
Go Together,
We Go Far and Grow Big