## Slide 1
Automation Testing
ZL Chen, SIoT DQA, Advantech

## Slide 2: Agenda
Benefits of Automation Testing
Develop the Automation Testing Tools
  Reliability Tools
  Process Tools
Continuous Integration Structure

## Slide 3: Benefits of Automation Testing
測試時間成本降低
長時間執行測試
程式控制執行
腳本重複調用
測試準確執行
Automation Testing Tools
Automation Testing

## Slide 4: Develop the Automation Testing Tools
Reliability Tools
Wi-Fi Frequency Switch Automation
Process Tools
Luminance Automation
Resolution Automation
Roaming Automation
Airplane ON/OFF Mode Automation
PXE Automatic Installation
ProgramIndex Automation

## Slide 5: Roaming Automation
  開發需求
    為了解決原先人工切換 AP 的測試方法
    希望可以利用程式控制 AP 介面做重新啟動，方可使待測物做漫遊動作
  軟體環境架構
    擬定 AP 切換環境，可透過程式做 AP 重啟並使待測物做漫遊切換
    漫遊示意圖請看下頁

## Slide 6
Trigger Handover
AP: A
AP: B
DUT
DUT
A dBm ↓, B dBm ↑
Repeat Mode
Trigger Handover
AP: A
DUT
DUT
B dBm ↓, A dBm ↑
A -> B
B -> A
AP: B
Repeat Mode

## Slide 7: Roaming Automation - Log
漫遊程式產生的紀錄檔如下：

## Slide 8: Roaming Automation
  執行效益
  可以模擬手動測試行為
  透過程式控制介面做 AP 漫遊切換動作
  透過程式自動儲存 Ping 記錄
  問題延伸
  由於重複透過程式將 AP 重啟，造成 AP 不穩定，目前只能執行最多十次
  解決方案
    可以嘗試透過數位衰減器嘗試解決 AP 自動重啟問題

## Slide 9: Continuous Integration Structure
PC
User
CI Server
Test Cases Server
DUT
6. Feedback Result
2. Trigger Jobs
3. Execute Test Script
1. Connect
5. Console Response
4. Run Test Script
7. Mail

## Slide 10
Go Together,
We Go Far and Grow Big