## Slide 1
Automation Testing
ZL Chen, SIoT DQA, Advantech

## Slide 2: Agenda
Automation Testing Functional
Automation Testing Tools
  Reliability Tools
  Process Tools
Continuous Integration Structure

## Slide 3: Automation Testing Functional
Cost Reduction
Repeatability
Programmable
Reusable
Quality
Reliability Tools
Process Tools
Implementation

## Slide 4: Automation Testing Tools
Reliability Tools
Wi-Fi Frequency Switch Automation
Process Tools
Luminance Automation
Resolution Automation
Roaming Automation
Airplane ON/OFF Mode Automation
PXE Automatic Installation
ProgramIndex Automation

## Slide 5: Roaming Automation
  開發需求
    為了解決人工手動切換 AP 的問題
    利用程式控制 AP 介面做重新啟動，方可使待測物做漫遊動作
  軟體環境架構
    必須在中繼模式下執行程式
    漫遊示意圖請看下頁

## Slide 6
Trigger Handover
AP: A
AP: B
DUT
DUT
A dBm ↓, B dBm ↑
Repeat Mode
Trigger Handover
AP: A
DUT
DUT
B dBm ↓, A dBm ↑
A -> B
B -> A
AP: B
Repeat Mode

## Slide 7: Roaming Automation - Log
漫遊程式產生的紀錄檔如下：

## Slide 8: Roaming Automation
  程式改善
  可以解決人為執行上的疏忽
  透過程式自動做 AP 漫遊切換動作
  透過程式自動儲存 Ping 記錄
  可以做長時間的壓力測試
  目前例外狀況
  由於使用 AP 重啟，所以 AP 漫遊穩定次數為十次
  可以透過數位衰減器嘗試解決 AP 自動重啟壽命

## Slide 9: Continuous Integration Structure
PC
User
CI Server
Test Cases Server
DUT
6. Feedback Result
2. Trigger Jobs
3. Execute Test Script
1. Connect
5. Console Response
4. Run Test Script
7. Mail

## Slide 10
Go Together,
We Go Far and Grow Big